## Slide 1: Analyzing and Leveraging Decoupled L1 Caches in GPUs
Mohamed Assem Ibrahim, Onur Kayiran, Yasuko Eckert, Gabriel H. Loh, Adwait Jog

## Slide 2: State of GPU Computing GPU Scaling Trends
GPU die sizes are getting larger
Core count is increasing as well
Chart: Year
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2013 | 2015
Area | 70 | 97 | 68 | 218 | 218 | 297 | 288 | 352 | 420 | 282 | 334 | 389 | 365 | 438 | 596
Wikipedia (Data)

## Slide 3: State of GPU Computing Challenges with Large-Scale GPUs
1 L1 bandwidth is underutilized
& L2 bandwidth is a bottleneck!
Network-on-Chip (NoC)
Core
L1
Core
L1
Core
L1
Core
L1
Core
L1
Core
L1
Core
Core
Core
L1
Core
L1
Core
L1
Core
L1
Reply
2 Replication of data (cache line) across L1 caches
L1
L1
Private
L1
L2
Memory
L2
Memory
L2
Memory
L2
Memory
L2

## Slide 4: Conventional Cache/NoC Hierarchy
Improving L1 bandwidth utilization and reducing data replication requires:
  NoC overhead to enable inter-core communication
  Disrupting the Home core
    Arbitration between local and remote requests
Core
L1
L2
Memory
NoC
Problem Source: Tightly-coupled GPU core and L1 cache!
Solution?

## Slide 5: Decoupled L1 Caches (DC-L1s)
A-1
A-2
Separate L1 cache from the GPU core.
  Break the tight-coupling!
0
1
2
…
NoC#1 (Core ↔ DC-L1)
NoC#2 (DC-L1 ↔ L2)
3
4
5
A-1
A-2
0
1
2
…
3
4
5
0
1
2
…
3
4
5
C-1
C-2
Lite GPU Core
(No L1 Cache)
DC-L1
(Decoupled L1)
L2+Memory
Level-1
Cache
Level-2
Cache
Two-level Cache
Hierarchy

## Slide 6: Aggregating DC-L1 Caches
2X
Size
0
Merge X DC-L1s to form one bigger DC-L1 cache.
  Reduced replication
  Better L1 bandwidth utilization
  Lower peak L1 bandwidth
L2
Lite Core
DC-L1
0
1
0
…
0
1
…
40x32 XBar
2x1 XBar
2
3
1
2x1 XBar
…
…
2x1 XBar
2x1 XBar
39
38
2
78
79
31
30
Aggregation Granularity?
1
Assume 80-core System with 80 DC-L1s
(Example of aggregating two DC-L1s)
Pr40 = Aggregate 2 DC-L1s
IPC Boost + Reduced Area/Power
Low Replication Reduction

## Slide 7: Shared DC-L1 Caches
39
38
2X
Size
Shared cache organization across DC-L1s.
  Eliminate replication.
Use 80x40 crossbar in NoC#1.
  Enable communication between a given core to all DC-L1 caches.
L2
Lite Core
DC-L1
0
1
0
…
0
1
…
40x32 XBar
80x40 XBar
2
3
1
…
2
78
79
31
30
Unique Addr. Range Slice
Assume 80-core System with 40 DC-L1s
(Aggregation Granularity = 2)
Sh40 = Significant IPC Boost
Area/Power Overheads + Poor-performing Applications

## Slide 8: Clustered Shared DC-L1 Caches
37
36
39
38
0
3
1
2
…
…
37
36
39
38
Shared cache organization across a cluster of DC-L1s.
  Eliminate replication within a cluster.
  Limit overall replication.
Use smaller crossbars in NoC#1.
  Enable communication between a given core to all DC-L1 caches in a cluster.
L2
Lite Core
DC-L1
0
1
…
0
1
…
10x8 XBar
8x4 XBar
7
…
…
8x4 XBar
7
31
24
Clusters Count?
…
…
Assume 80-core System with 40 DC-L1s
(Aggregation Granularity = 2)
Unique Addr. Range Slice
79
72
73
10x8 XBar
C0
C1
C2
C3
C9
C0
C1
C2
C3
C9
2
25
26
1
0
3
2
31
24
25
26
7
0
1
2
Sh40+C10 = Choose 10 Clusters
IPC Boost + Replication Reduction + Reduced Area/Power

## Slide 9: Frequency-boost Optimization
Smaller Crossbars = Higher Operating Frequency
Optimization  Double the NoC frequency in NoC#1
0
1
0
8x4 XBar
7
3
1
…
2
Chart: Crossbar
| 2x1 | 8x4 | 40x32 | 80x32 | 80x40
Max. Freq (MHz) | 3533.0071 | 2240.3943 | 799.335 | 496.4257 | 483.992
Sh40+C10+Boost

## Slide 10: Evaluation IPC
Chart: 
Pr40 | 0.66185 | 0.79764 | 0.80615 | 0.83434 | 0.8682 | 0.86991 | 0.89487 | 0.89769 | 0.93186 | 0.93234 | 0.93889 | 0.94952 | 0.95139 | 0.95606 | 0.95874 | 0.9642 | 0.96505 | 0.96651 | 0.98474 | 0.99167 | 1.0011 | 1.0079 | 1.2164 | 1.296 | 1.3959 | 1.6081 | 1.668 | 1.9992
Sh40 | 0.15289 | 0.48809 | 0.52723 | 0.55583 | 0.60381 | 0.95583 | 0.96512 | 0.96746 | 0.97026 | 0.97227 | 0.98259 | 0.99167 | 0.99614 | 1.0546 | 1.0588 | 1.06 | 1.0803 | 1.1503 | 1.2068 | 1.2382 | 1.2587 | 1.298 | 1.396 | 1.6059 | 1.638 | 1.9341 | 2.3611 | 2.9459
Sh40+C10+Boost | 0.86313 | 0.90708 | 0.93805 | 0.94744 | 0.94874 | 0.96871 | 0.96974 | 0.97895 | 0.9902 | 0.9925 | 0.99659 | 1.0078 | 1.0139 | 1.0164 | 1.0179 | 1.0325 | 1.132 | 1.2072 | 1.2877 | 1.2884 | 1.3145 | 1.3203 | 1.3501 | 1.4372 | 1.9582 | 2.0575 | 5.0231 | 8.0233
Chart: 
| C-RAY | C-NN | P-2DCONV | P-3MM | P-GEMM | Mean
Pr40 | 0.8682 | 0.79764 | 0.66185 | 0.86991 | 0.83434 | 0.80242
Sh40 | 0.15289 | 0.55583 | 0.48809 | 0.60381 | 0.52723 | 0.42087
Sh40+C10+Boost | 0.90708 | 0.94874 | 0.94744 | 0.9902 | 0.93805 | 0.94593
Chart: 
| C-BFS | C-BFS2 | R-CFD | S-QTC | S-Reduction | S-Triad | P-3DCONV | P-2MM | P-SYRK | T-AlexNet | T-ResNet | T-SqueezeNet | Mean
Pr40 | 0.9642 | 0.89487 | 0.98474 | 0.93234 | 0.80615 | 0.89769 | 0.93186 | 1.668 | 1.3959 | 1.9992 | 1.296 | 1.6081 | 1.147
Sh40 | 1.396 | 1.2382 | 1.2587 | 1.6059 | 1.2068 | 1.1503 | 0.97227 | 1.06 | 2.3611 | 2.9459 | 1.638 | 1.9341 | 1.4797
Sh40+C10+Boost | 1.4372 | 1.3501 | 1.3203 | 1.2884 | 0.86313 | 1.2072 | 1.3145 | 1.9582 | 1.132 | 8.0233 | 2.0575 | 5.0231 | 1.7511
Chart: 
| C-BLK | C-LIB | C-LPS | C-NQU | C-RAY | C-STO | C-SLA | C-CONS | C-FWT | C-TRA | C-BFS | C-NN | C-JPEG | C-BFS2 | C-AES | C-Kmeans | R-BP | R-BFS | R-HS | R-CFD | R-SC | R-NW | R-LUD | S-QTC | S-Reduction | S-Scan | S-Stencil2D | S-Triad | P-2DCONV | P-3DCONV | P-2MM | P-3MM | P-FDTD-2D | P-GEMM | P-SYRK | T-AlexNet | T-ResNet | T-SqueezeNet | Mean | Mean | Mean
Pr40 | 0.95874 | 0.94952 | 0.95139 | 0.99167 | 0.8682 | 0.90903 | 0.97548 | 0.94317 | 1.0011 | 0.91094 | 0.9642 | 0.79764 | 0.92637 | 0.89487 | 0.95606 | 0.78165 | 0.93889 | 0.91327 | 0.96651 | 0.98474 | 1.2164 | 1.0079 | 0.96505 | 0.93234 | 0.80615 | 0.94839 | 0.87171 | 0.89769 | 0.66185 | 0.93186 | 1.668 | 0.86991 | 0.9672 | 0.83434 | 1.3959 | 1.9992 | 1.296 | 1.6081 | 0.9872 | 1.147 | 0.92118
Sh40 | 0.98259 | 0.95583 | 1.0803 | 0.99167 | 0.15289 | 0.89871 | 0.99194 | 1.0161 | 0.99614 | 1.0828 | 1.396 | 0.55583 | 0.93071 | 1.2382 | 0.96512 | 0.96611 | 0.97026 | 0.89667 | 1.0588 | 1.2587 | 1.298 | 1.0546 | 0.96746 | 1.6059 | 1.2068 | 1.3426 | 0.91761 | 1.1503 | 0.48809 | 0.97227 | 1.06 | 0.60381 | 0.96123 | 0.52723 | 2.3611 | 2.9459 | 1.638 | 1.9341 | 1.0155 | 1.4797 | 0.85352
Sh40+C10+Boost | 0.97895 | 0.96974 | 1.0164 | 0.99659 | 0.90708 | 0.94715 | 0.97941 | 0.98743 | 1.0139 | 0.9655 | 1.4372 | 0.94874 | 0.95581 | 1.3501 | 1.0078 | 0.85986 | 0.96871 | 0.95825 | 1.0325 | 1.3203 | 1.2877 | 1.0179 | 0.9925 | 1.2884 | 0.86313 | 1.1037 | 0.89901 | 1.2072 | 0.94744 | 1.3145 | 1.9582 | 0.9902 | 0.93315 | 0.93805 | 1.132 | 8.0233 | 2.0575 | 5.0231 | 1.1788 | 1.7511 | 0.98205
Results are normalized to Private L1 organization baseline.
Replication-sensitive Applications  Average = +75%, Max = +8X
Poor-performing Applications  Average = -5%
Poor-performing
Replication-sensitive
8x
5x
75%
More results in the paper!

## Slide 11: Conclusions
Observe an opportunity for decoupled L1 caches in GPUs to break the tight coupling between the GPU cores and the L1 caches
  Reduce data replication across the L1 caches
  Improve L1 bandwidth utilization
Achieved through the following:
  Aggregated DC-L1 caches to improve the L1 bandwidth utilization
  Clustered Shared DC-L1 caches to limit data replication
Results
  75% IPC improvement for the replication-sensitive applications
  5% IPC degradation for the poor-performing replication-insensitive applications
  50% NoC area reduction because of the hierarchical design

## Slide 12: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2021 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. Other names are for informational purposes only and may be trademarks of their respective owners.

## Slide 13
* We acknowledge the support of the National Science Foundation (NSF) CAREER award #1750667.
* This presentation and recording belong to the authors. No distribution is allowed without the authors' permission.
Mohamed Assem Ibrahim
maibrahim@email.wm.edu
https://massemibrahim.github.io/
Thank You! Questions?